PASSPORT

LED Explosion-proof Light Fixture of

«SPV-220-005» type

KENS.676253.112 PS

1 General Information

1.1 LED Explosion-proof light fixture of «SPV-220-005» type (further named as the light) of the white emission is used for operating in the AC supply for outdoor and indoor illumination of industrial objects. The application area – explosive zones 1,2 according to IEC 60079-10-1, dangerous zones 21,22 for combustible dust according to IEC 60079-10-2, explosion-proof marking according to IEC 60079-14. The light consists of the housing-radiator, LED module, the driver, the PCB, the contact device. The bracket fitting is provided with the light.

Ex marking for explosive gas/dust atmospheres:

- TR CU: 1 Ex d e IIC T5 Gb/ Ex tb IIIC Т95(С Db;

- IECEx: 1 Ex d e op is IIC T5 Gb/ Ex tb IIIC Т95(С Db;

- АТЕХ: II 1 G Ex d e IIC T5 Gb/ III 1 D Ex tb IIIC T95°C Db.

1.2 The light preserves its working capacity at the following conditions:

- HR up to 95% (at the temperature +40 ̊С);

- ambient operating temperature from minus 40 ̊С up to plus 50 ̊С, for the light usage in T5 temperature class.

1.3 Technical data of the light:

- supply voltage 220 VAC, frequency 50 Hz. The supply voltage range is 176 ÷ 264 VAC (50±10% Hz) or 250 ÷ 370 VDC;

- the light electrical and illuminating parameters must correspond to the values given in Table 1.

Table 1

| The light type | Light flux*, not less than, lm | Consumption power, nominal**, W |
| --- | --- | --- |
| SPV-220-005-01 | 2800 | 20 |
| SPV-220-005-02 | 4200 | 30 |
| SPV-220-005-03 | 5600 | 40 |
| SPV-220-005-04 | 8400 | 60 |

* Light flux is specified for the LED module at the chip temperature of 25 C. To specify the light flux it is necessary to consider IES-file for the light.

** Consumption power value can differ by 10%.

- color temperature, К: N - (normal emission) 4 000 ÷6 000;

- ripple factor of the light flux is not more than 10%;

- IP up to IEC 529 is not worse than IP65;

- climatic performance MCC, placement category 1 up to IEC 60721-2-1:2013:1982, IEC 60068-1:2013;

- electric shock protection class 1 up to IEC 60598-1;

- insulation resistance of live parts is not less than 20 МОm;

- grounding resistance is not more than 0,5 Оm;

- power factor is not less than 0,9;

- the light weight must correspond to the values given in Table 2.

Table 2

| The light type | The light weight, kg, not more than |
| --- | --- |
| SPV-220-005-01 | 4,5 |
| SPV-220-005-02 | 4,5 |
| SPV-220-005-03 | 4,5 |
| SPV-220-005-04 | 4,5 |

1.2.19 The outward, design and dimensions of the light are shown on pic. 1,2,3:

Pic. - 1

Pic. – 2

Pic. – 3

1 – LED module; 2 - ring; 3 - connector; 4 – blind plug; 5 – contact device; 6 – driver; 7 – glass;

8 – gasket ring; 9 – bracket; 10 – lid; 11 – cable gland; 12 – lid; 13 – housing.

- fire safety is up to NPB 249-97, IEC 60598-1;

- service life when conforming to operating conditions is not less than 10 years;

- storage from the date of its being manufactured is 3 years.

2. SET (the light completeness):

2.1 The set consists of:

- a light – 1 pce.,

- an operating manual – 1pce.,

- a passport – 1 pce.,

- a bracket – 1 pce.,

- a certificate copy and a certificate annex copy – 1 pce.,

- a package – 1 pce.

3. Acceptance Certificate

3. 1 The light is manufactured in accordance with specifications TS 3461–018–41677105–2016 and proved to be suitable for operating.

Stamp_______ (Signature)	 __________(Signature clarification)

QCD

Plant No.___________ 	Issue Date_____________________

4. Recycling Data

4.1 All the materials of which the light is manufactured are not dangerous for the life and health of people and the environment and are in conformance with IEC 60598-1.

4.2 On completing the operation of the light, it does not require a special recycling and should be handed as a recyclable material in accordance with the present rules.

5. Warranty

5.1  The manufacturer guarantees the conformance of the light to the technical specifications and normal work within 5 years since operating it at condition of observing the rules of transportation, storage and installation.

5.2 Within the warranty period damaged lights should be changed charge free by the manufacture at the conditions of the conformance to the installation and operating rules by the customer.

6. Reclamation Data

6.1 The order of claiming a reclamation is stated in accordance with the current regulations on the objects of applying.

6.2 The reclamation in a standard form should be claimed to the manufacturer with a compulsive attachment of a discarding act, without which the reclamation cannot be accepted. The reclamation should be forwarded the following address:

19, Leskova str., Orel, 302040, Russia, JSC «Proton»

Tel./ Fax. (4862) 41-44-03

| Place in service date | Practitioner name | Practitioner signature | Notes |
| --- | --- | --- | --- |